SERIAL PROTOCOL FOR AGRIGEL

REVISION HISTORY

2017/09/14 – H914 – Add PumpRPM from Master to Slave for Hub

2016/10/27 – GA27 – Provisionally reserve bit 4 of the slave flags
        for the new SlaveDisable flag we are trying to
        implement

2016/08/11 – G811 – Add note about SLAVE addresses for RS485 bus 2

2016/06/23 – G623 – Specify a structure which allows the hub to a
        assign slave numbers to the slaves, based on
        which hub they are connected to and where on
        the hub they are connected, so that we can
        still send each packet to every slave in order
        to swiftly distribute flow settings across the
        whole network
        - COMMAND - 0001 – Use DIP switch address
        - COMMAND - 0010 – Use assigned address
        - Add the EEPROM memory map to specify how
        we are currently using the EEPROM and where
        the assigned address can be stored

2016/06/09 – G609 – Change the format of the [Response] to
        include the [Payload] length to ease the
        implementation of the hub code

2016/05/26 – G526 – Add another issue to the list
        - Tie down the specification for the hub data
        going to the main unit

2016/05/25 – G525 – Document some issues which I have become aware
        of while implementing the hub code

2016/05/12 – G512 – Added a broadcast address for the hubs
        - Allocate addresses for the slaves on the
        second RS485 port
        - Allocate addresses for in case we use 8 hubs
        instead of 4, to give us a total of 64 slaves
        per bus, instead of only 32

2016/04/06 – G406 – Fill out the hub memory map

2016/03/31 – G331 – Add hub addressing
        - Add hub memory map – needs filling in

2016/01/29 – G129 – Add support for re-flashing firmware

2015/12/10 – FC10 – Add open kick value to packet

2015/10/29 – FA29 – Add FreezeStepperMotor flag from the main unit

2015/04/23 – F423 – Added 2 new flags Interrupt 1 – level and
        Interrupt 2 – level and moved the Interrupt 1
        flags from Flags to Flags2

2015/04/17 – F417 – Added CalibrationKeyUnlock flag to the data
        from the MASTER to the SLAVE
            - Changed the name of FlowCalibrationValue to
              FlowMeterCalibration to match source code

2015/03/26 – F326 – Added FlowCalibrationValue to the data
        from the SLAVE to the MASTER

2015/03/19 – F319 – Add the following data from the
        SLAVE to the MASTER:
        - Flags2
        - MCP3021Reading
        - VersionYM
        - VersionDD
        - Moved the Interrupt1* variables,
        (they have not been used in the Main Unit yet)

2014/10/23 – EA23 – Changes made, but not documented in this list

2013/10/10 – DA10 – Changed the checksum calculation in this
        document to match the program
            - Minor cosmetic layout changes for clarity
2012/12/13 – CC13 – Revision history not yet implemented

2012/08/30 – C830 – Revision history not yet implemented

2012/06/28 – C628 – Revision history not yet implemented

KNOWN ISSUES

2016/05/26 – G526 – The packet writes and reads don't actually use
        the addresses sent in the packets! I think
        the addresses the main unit sends are swapped
        around and we directly access the memory as
        per the specification.

2016/05/25 – G525 – The START, (address) is not incorporated in
        the checksum, so if only the START byte is
        corrupted, the packet could be received and
        executed by the incorrect slave.
            - The CHECKSUM is not received and verified
        if bits 4 and 5 of the COMMAND are set,
        (direct command). It seems to be working
        OK the way it is, but it would be better to
        implement it correctly at some stage.

SERIAL PORT SETTINGS

9600 9N1 (with hardware address detection)

At this speed each byte takes 1msec, if the need arises this speed may be increased.

MASTER command packet

[Start][Command][Payload][Checksum]

The MAIN unit is the MASTER and initiates communication with each SLAVE in turn.

SLAVE response packet

[Start][Response][Payload][Checksum]

The SLAVES listen for command packets from the MASTER and then respond appropriately, if it is present.

[Start]

The START byte is different to any other byte in the protocol in that it's ninth bit is set, (1). In that way I can use the hardware address detect feature to maintain synchronisation and minimise unnecessary communication interrupts.

The MASTER is address 0, (1)00000000.

The SLAVEs are numbered from address 1, (1)00000001, upwards to address 32, (1)00100000. Addresses from 33, (1)00100001, upwards to address 64, (1)01000000, are reserved for future expansion to RS485 bus 1 using 8 HUBs instead of 4.

The HUBs are numbered from address 70, (1)01000110, upwards to address 77, (1)01001101.

Address 85, (1)01010101, will be recognised as being a broadcast from the MASTER to all of the SLAVEs, and is chosen because of its distinctive bit pattern.

Address 90, (1)01011010, will be recognised as being a broadcast from the MASTER to all of the HUBs, and is chosen because of its distinctive bit pattern

Addresses from 129, (1)10000001, upwards to 192, (1)11000000, are reserved for 64 slaves on RS485 bus 2, (although they could use the same addresses because they are on a different bus).

[Command]

There are 2 categories of commands NORMAL and FAST. I do not usually detail any NORMAL commands for projects as I haven't found a need for them yet, but they do provide a back door for future expansion, for things that the FAST commands may not handle.

     FAST command format

7 6 5 4 3 2 1 0
     | | -+- ---+---
     | | | |
     | | | +----- Number of bytes to be read/written
| | | - It doesn't make much sense to write or
     | | | read 0 bytes, so 0-15 represents 1-16
     | | |
     | | +----------- Location to read/write
| | 00 = RAM
     | | - See RAM memory maps
     | | 01 = Internal EEPROM
     | | - See EEPROM memory map
     | | 10 = Internal FLASH
     | | - Verify that we are only writing
     | | to the upper half of program
     | | memory – (which is where the
     | | program is buffered, before it is
     | | used to re-flash the micro, once
     | | it has been verified)
     | | 11 = Treat lower 4-bits as command
| | to be executed
     | | - 0000
     | | - 0001 – Use DIP switch address
     | | - This will be broadcast
     | | by the MAIN UNIT to the
     | | SLAVES
     | | - Old SLAVES will use
     | | the DIP switches to
     | | determine their address
     | | - The HUB will filter out
     | | this broadcast, as it
     | | will assign addresses
     | | to the SLAVES
     | | - 0010 – Use assigned address
     | | - This will be broadcast
     | | by the HUB to the SLAVES
     | | - 0011
     | | - 0100
     | | - 0101
     | | - 0110
     | | - 0111
     | | - 1000
     | | - 1001
     | | - 1010
     | | - 1011
     | | - 1100 = Re-flash firmware
     | | - 1101
     | | - 1110
     | | - 1111
     | |
     | +-------------- 0 = Write
     | 1 = Read
     |
     +---------------- 0 = Fast command
        1 = Normal command

[Payload]

Depends on the command.

For FAST commands the length of the data is embedded in the command, so the length of the payload is determined as follows:

n+1+2

Where:
  n is the number extracted from the low nibble
    of the command
  +1 because 0-15 represents 1-16
  +2 because an address must be supplied for the data

For a WRITE the payload consists of the starting address of the block to be written followed by the data to be written.

For a READ command the payload only consists of the starting address of the block to be read.

[Checksum]

The Checksum is the 1's complement of the 8-bit sum of all the bytes from the command/response to the last byte of the payload.

[Response]

The SLAVEs do not respond to broadcast packets, (i.e. packets sent to address 0x55 or 0x5A).

7 6 5 4 3 2 1 0
     | -+- | --+---
     | | | |
     | | | +----- Number of bytes to be read/written
| | | - It doesn't make much sense to write or
     | | | read 0 bytes, so 0-15 represents 1-16
     | | |
     | | +--------- Byte Count Multiplier
     | | - This bit is required because some
     | | responses do not include a [Payload]
     | | - 0 = Number of bytes x0
     | | - 1 = Number of bytes x1
     | |
     | +------------ Normal Response code:
     | | - 00
     | | - 01 = Normal
     | | - 10
     | | - 11
     | |
     | +------------ Error Response code:
     | - 00
     | - 01 = General failure
     | - 10 = Checksum failed
     | - 11 = Unrecognised command
     |
     +---------------- 0 = Normal response
        1 = Error response

There is always a debate about whether to respond with negative responses or not, especially things like C0H, (checksum failed), because the correct SLAVE could have received the packet correctly and could be responding with data, which another SLAVE which received a corrupt packet, could be corrupting by sending a negative response!

I think in this implementation the MAIN unit will simply time out, in other words if it doesn't receive a positive response from the SLAVE it addressed within a specified time then it will assume that the SLAVE didn't receive the packet OR the SLAVE did receive the packet and the MASTER didn't receive the response, in either case the MASTER can try to re-establish communication periodically.

SLAVE RAM MEMORY MAP

This is a starting point, it may change as the implementation progresses, because of the nature of the protocol it is a simple task to add or subtract variables as required:

RAM data from MASTER to SLAVES:

0x010(0) FlowSetPoint
0x010(1) FlowSetPointH
        - in ml/min
0x010(2) Flags
        - Bit 7
        - Bit 6
        - Bit 5
        - Bit 4 – Provisionally reserved - SlaveDisable
        - Bit 3
        - Bit 2 – Freeze stepper motor
        - Bit 1 – Calibration unlock
        - Bit 0 – Control flow
0x010(3) FlowCompensation
        - Flow * FlowCompensation / 100
0x010(4) OpenKick
0x010(5) OpenKickH
        - in steps
0x010(6) PumpRPM (Hub port record only)
0x010(7) PumpRPMH (Hub port record only)
0x010(8)
        0x010(9)
        0x010(A)
        0x010(B)
        0x010(C)
        0x010(D)
        0x010(E)
        0x010(F) Flow meter calibration value

RAM data from SLAVES to MASTER:

0x011(0) FlowProcessVariable
0x011(1) FlowProcessVariableH
0x011(2) Flags:
        - Bit 7 – Flow error – I2C - UFO2
        - Bit 6 – Flow error – I2C - EEPROM
        - Bit 5 – Flow error – ultrasonic sensor
        - Bit 4 – Flow – new reading
        - Bit 3 – Interrupt 2 - over flow
        - Bit 2 – Interrupt 2 - new reading
        - Bit 1 – Interrupt 2 – level
        - Bit 0 –
        0X011(3) Interrupt2Time
        0X011(4) Interrupt2TimeH
        0X011(5) Interrupt2TimeHH
        0X011(6) Interrupt2Count
        0X011(7) Flags2:
        - Bit 7 –
        - Bit 6 –
        - Bit 5 – Interrupt 1 – over flow
        - Bit 4 – Interrupt 1 – new reading
        - Bit 3 – Interrupt 1 - level
        - Bit 2 – VersionY0
        - 0 = 2000 to 2015
        - 1 = 2016 to 2031
        - Bit 1 – MCP3021 – I2C error
        - Bit 0 – MCP3021 - new reading
        0X011(8) MCP3021Reading
        0X011(9) FlowMeterCalibration
        0X011(A) Interrupt1Time
        0X011(B) Interrupt1TimeH
        0X011(C) Interrupt1TimeHH
        0X011(D) Interrupt1Count
        0X011(E) VersionYM
        0X011(F) VersionDD

SLAVE EEPROM MEMORY MAP

This is a starting point, it may change as the implementation progresses, because of the nature of the protocol it is a simple task to add or subtract variables as required:

EEPROM data from MASTER to SLAVES and SLAVE to MASTER:

0x010(0) EE_ValveNumber (as set by the DIP switches)
0x010(1) EE_FlowCompensation
0x010(2) EE_ProgramMemorySmudged
0x010(3) EE_AssignedValveNumber
0x010(4) EE_NonVolatileFlags
0x010(5)
0x010(6)
0x010(7)
0x010(8)
        0x010(9)
        0x010(A)
        0x010(B)
        0x010(C)
        0x010(D)
        0x010(E)
        0x010(F)

HUB RAM MEMORY MAP

This is a starting point, it may change as the implementation progresses, because of the nature of the protocol it is a simple task to add or subtract variables as required:

RAM data from MASTER to HUBS:

0x010(0) Flags
        - Bit 7 –
        - Bit 6 –
        - Bit 5 –
        - Bit 4 –
        - Bit 3 –
        - Bit 2 –
        - Bit 1 –
        - Bit 0 – Spare I/O
0x010(1)
0x010(2)
0x010(3)
0x010(4)
0x010(5)
0x010(6)
0x010(7)
0x010(8)
        0x010(9)
        0x010(A)
        0x010(B)
        0x010(C)
        0x010(D)
        0x010(E)
        0x010(F)

RAM data from HUBS to MASTER:

        0x010(0) Flags
        - Bit 7 – VersionY0
        - 0 = 2000 to 2015
        - 1 = 2016 to 2031
        - Bit 6 – Pickup – over flow
        - Bit 5 – Pickup – new reading
        - Bit 4 – Pickup - level
        - Bit 3 – Engaged - level
        - Bit 2 – Spare I – (labelled RADAR)
        - Bit 1 – Spare I/O
        - Bit 0 –
0x011(1) – PickupTime
0x011(2) - PickupTimeH
0x011(3) - PickupTimeHH
0x011(4) - PickupCount
0x011(5) - Pressure
0x011(6) - AnalogueLow
0x011(7) – SpareAnalogue
0x011(8) – DIP switches
        - Bit 7:4 - hub number
        - Bit 3:0 – port count
        0x011(9) – LEDs units 1 to 4
        0x011(A) – LEDs units 5 to 8
        0x011(B) – LEDs voltages
        0x011(C) – LEDs hub and spare
        0x011(D) -
        0x011(E) - VersionYM
        0x011(F) - VersionDD

EXAMPLES

For the MASTER to set all of the parameters on all of the SLAVEs simultaneously:

Command from MASTER:

55 08 01 00 Flags FSPH FSP PH P SH S CH C CheckSum

Response from SLAVEs:

None, this was a broadcast packet from the MASTER

For the MASTER to set all the parameters on SLAVE number 17:

Command from MASTER:

17 08 01 00 Flags FSPH FSP PH P SH S CH C CheckSum

Response from SLAVEs:

00 20 DF

For the MASTER to set the calibration parameter on SLAVE number 3:

Command from MASTER:

03 01 01 07 CH C CheckSum

Response from SLAVEs:

00 20 DF

For the MASTER to verify all the parameters on SLAVE number 25:

Command from MASTER:

25 48 01 00 CheckSum

Response from SLAVEs:

00 38 Flags FSPH FSP PH P SH S CH C CheckSum

For the MASTER to read the flow rate on SLAVE number 8:

Command from MASTER:

08 41 01 10 CheckSum

Response from SLAVEs:

00 31 FPVH FPV CheckSum

*** END OF DOCUMENT ***